### analogguru:

Soda hier was semi-"parametrisches" oder auch sweep-eq genannt...so ziemlich der einfachste, den es gibt, und die Teile gibts beim Klaus im Shop, soweit ich weiß.

VR3 und VR5 sind Stereo-Potis 100k neg. log.

Im Prinzip kann man jede OP-Stufe einzeln nehmen...

IC-3B ist für die Höhen

IC-4A ist ein Mittenregler für veränderbare Frequenz und Anhebung/Abschwächung

IC-4B detto

IC 5A ist ein Bassregler

Die ursprüngliche Schaltung stammt aus einen Soundcraft Mischpult (Serie 6000) und war für +/-15 Volt daher das komische Masse-Symbol für die U/2.

Ist links unten mit den 2 Widerständen und dem Elko realisiert, damit es mit 9V auch geht.

### http://www.prodigy-pro.com/forum/viewtopic.php?p=39648#39648:

IMHO the OP2604 sounds MUCH better in Soundcrafts, Tridents, and DDAs.

or, if you want a softer, 'tubier' sound, try the opa134.

EDIT; the 2604s can become very expensive for a whole console ! the LM833 and 5532 are also be great options, so pick your battles wisely

### http://forum.musikding.de/yabbse/index.php?topic=6650.msg71149#msg71149

Bei den Op-Amps wäre es optimal die OPA2607
(BURR BROWN) einzusetzen. Sind zwar teuer, machen aber eindeutig am 
meisten Druck.